## Slide 1
AZ-500 • SKILL 2.1
Virtual Network Security
NSGs & ASGs, UDRs, VNet Peering, VPN Connectivity, Virtual WAN, ExpressRoute Encryption, PaaS Firewalls & Network Watcher
Joe Poyzer
Network & Security Engineering

## Slide 2
AGENDA
Nine Topics, One Exam Skill
1. Network Security Groups
2. Application Security Groups
3. User-Defined Routes
4. VNet Peering & Hub-Spoke
5. VPN Gateway & Authentication
6. Point-to-Site / Site-to-Site
7. Virtual WAN
8. Encryption over ExpressRoute
9. PaaS Firewalls & Network Watcher
AZ-500 Skill 2.1 — Virtual Network Security
1

## Slide 3
NETWORK SECURITY GROUPS
Where NSGs Apply — and the Order They're Evaluated
An NSG filters traffic with allow/deny rules — think of it as a modern equivalent to a VLAN in a physical network.
Two places to apply an NSG
On a subnet — one rule set secures everything in it
On a network interface (NIC) — per-VM control
Both can be used together on the same path
Evaluation order matters
Inbound traffic: subnet NSG rules evaluated first, then NIC NSG rules
Outbound traffic: NIC NSG rules evaluated first, then subnet NSG rules
Traffic stops evaluating as soon as one rule matches
Applying NSGs at both levels means traffic is checked twice — know the order, or you'll debug the wrong layer.
AZ-500 Skill 2.1 — Virtual Network Security
2

## Slide 4
NETWORK SECURITY GROUPS
Rule Parameters (the 5-Tuple + Metadata)
Parameter | Notes
Name | Rule identifier
Priority | 100–4096. Lower number = higher priority = evaluated first. Stops at first match.
Source | IP address, CIDR block, Service Tag, or Application Security Group
Destination | IP address, CIDR block, Service Tag, or Application Security Group
Protocol | TCP, UDP, ICMP, or Any
Port Range | A single port, or a range
Action | Allow or Deny
Priority is the whole game — the lowest-numbered matching rule wins, full stop.
AZ-500 Skill 2.1 — Virtual Network Security
3

## Slide 5
NETWORK SECURITY GROUPS
Default Rules — Auto-Created, Cannot Be Deleted
Inbound
Name | Pri. | Action
AllowVNetInBound | 65000 | Allow
AllowAzureLoadBalancerInBound | 65001 | Allow
DenyAllInbound | 65500 | Deny
Outbound
Name | Pri. | Action
AllowVnetOutBound | 65000 | Allow
AllowInternetOutBound | 65001 | Allow
DenyAllOutBound | 65500 | Deny
These rules can't be removed — only overridden by adding a rule with a lower priority number. AllowVNetInBound is exactly why peered VNets are not segmented by default.
Removing a rule that allowed an existing connection doesn't necessarily kill it instantly — an interruption only happens once there's no traffic in either direction for a few minutes
AZ-500 Skill 2.1 — Virtual Network Security
4

## Slide 6
NETWORK SECURITY GROUPS
Creating and Associating an NSG
Portal steps
Network Security Groups → Add
Set Subscription / Resource Group / Name / Region
Review + Create → Go To Resource
Inbound Security Rules → Add — set Source, Destination, Port, Protocol, Action, Priority, Name
Subnets → Associate — pick VNet, then subnet
PowerShell
New-AzNetworkSecurityGroup -Name "AZ500NSG" \
-ResourceGroupName "AZ500RG" -Location "westus"
New-AzNetworkSecurityRuleConfig -Name ftp-rule \
-Access Allow -Protocol Tcp -Direction Inbound \
-Priority 100 -SourceAddressPrefix * \
-SourcePortRange * -DestinationAddressPrefix * \
-DestinationPortRange 21
An NSG does nothing on its own — it has no effect until it's associated to a subnet or a NIC.
AZ-500 Skill 2.1 — Virtual Network Security
5

## Slide 7
APPLICATION SECURITY GROUPS
Grouping by Role, Not by IP Address
An ASG lets you group VMs by application role and use that group — not a hardcoded IP — as the source or destination in an NSG rule.
What it buys you
An extra micro-segmentation layer on top of NSGs
Fewer NSGs needed overall — one NSG can cover multiple subnets, with ASGs doing the fine-grained split
Supports a Zero Trust posture — only explicitly permitted application flows are allowed
The rule that trips people up
You can use one ASG as the source and one ASG as the destination per rule
You cannot specify multiple ASGs on either side of the same rule
A VM with multiple workloads (e.g., web + SQL) can belong to multiple ASGs — each gets its own access rules
Rules that reference a role instead of an IP keep working as the environment grows — that's the whole payoff.
AZ-500 Skill 2.1 — Virtual Network Security
6

## Slide 8
APPLICATION SECURITY GROUPS
Creating and Associating an ASG
Portal steps
Application Security Groups → Create
Set Subscription / Resource Group / Name / Region → Review + Create
Go to the target VM → Networking → Network Settings
Configure (Application Security Group) → Add Application Security Groups → select the ASG
PowerShell
New-AzApplicationSecurityGroup \
-ResourceGroupName "MyRG" -Name "MyASG" \
-Location "West US"
Once created, the ASG shows up as a selectable Source/Destination option the next time you build or edit an NSG rule.
AZ-500 Skill 2.1 — Virtual Network Security
7

## Slide 9
USER-DEFINED ROUTES
VNets, Subnets & Azure's Default System Routes
A VNet is scoped to a single region — cross-region connectivity needs VNet Peering. Every subnet gets a routing table automatically.
Routes Azure creates for you
One route per VNet address range → next hop = Virtual network
Internet default: 0.0.0.0/0 → Internet, unless the destination is an Azure service — then it's routed over Azure's backbone instead
Default routes also exist for 10.0.0.0/8, 192.168.0.0/16, and 100.64.0.0/10
Routes Azure adds automatically when you...
Create VNet Peering → a route per peered address range
Add a Virtual Network Gateway → route(s) with the gateway as next hop
Enable a Service Endpoint → the service's public IPs get added to the route table
Next Hop Type = None means traffic is silently dropped
A route table only needs the routes that override the defaults — Azure already handles VNet and Internet reachability on its own.
AZ-500 Skill 2.1 — Virtual Network Security
8

## Slide 10
USER-DEFINED ROUTES
When and How to Create a Custom Route
Only create a custom route to override default behavior — classic case: point 0.0.0.0/0 at a firewall or NVA so it can inspect traffic first.
Valid next-hop types
Virtual appliance
Virtual network gateway
None (drop)
Virtual network
Internet
# 1. Create the route table
New-AzRouteTable -Name 'AZ500RouteTable' \
-ResourceGroupName ContosoCST -Location EastUS
# 2. Add a route to it
Get-AzRouteTable ... | Add-AzRouteConfig \
-Name 'ToAZ500Subnet' -AddressPrefix 10.0.1.0/24 \
-NextHopType 'MyVirtualAppliance' \
-NextHopIpAddress 10.0.2.4 | Set-AzRouteTable
# 3. Associate to a subnet
Set-AzVirtualNetworkSubnetConfig ... -RouteTable $rt
A subnet can be linked to only one route table. On conflict, user-defined routes win over default system routes.
AZ-500 Skill 2.1 — Virtual Network Security
9

## Slide 11
VNET PEERING & HUB-SPOKE
Connecting VNets — and the Four Peering Options
Peered traffic never touches a gateway or the public Internet — it's routed directly over the Microsoft backbone.
Option | What it does
Allow [VNet] to access the peered VNet | Default on — basic bidirectional reachability (hub-spoke communication)
Allow [VNet] to receive forwarded traffic from the peered VNet | Lets traffic that arrived at the peered VNet from elsewhere continue into this VNet (doesn't create UDRs/NVAs itself)
Allow gateway/route server to forward traffic to the peered VNet | Only relevant if this VNet has a gateway or route server
Enable use of the peered VNet's remote gateway/route server | Peered VNet must have a gateway and have this enabled on its side — only one side of the peering can enable it
All four options are independent toggles — enabling one doesn't imply the others. Hub-spoke designs typically need at least the first two.
AZ-500 Skill 2.1 — Virtual Network Security
10

## Slide 12
VNET PEERING & HUB-SPOKE
PowerShell, Same-Region vs. Global, and the Hub-Spoke Pattern
Add-AzVirtualNetworkPeering \
-Name 'NameOfTheVNetPeering' \
-VirtualNetwork SourceVNet \
-RemoteVirtualNetworkId RemoteVNet
Region scope
Same region: latency matches being inside a single VNet
Cross-region peering is called Global VNet Peering
Hub-spoke pattern
The hub is the central connectivity point to on-premises
Spokes peer to the hub, gaining isolation/security boundaries from each other
A site-to-site connection needs a dedicated GatewaySubnet in the hub
All on-prem traffic flows through that gateway subnet
The GatewaySubnet is not optional — Azure won't deploy a gateway without one, and that subnet can't be reused for anything else.
AZ-500 Skill 2.1 — Virtual Network Security
11

## Slide 13
VPN GATEWAY & AUTHENTICATION
Gateway Fundamentals and Connection Types
A gateway is two or more managed VMs in a dedicated GatewaySubnet — one gateway per VNet, and its type is VPN or ExpressRoute, never both.
Type | Use case | Protocol
Point-to-Site (P2S) | Individual remote users connecting to the VNet | SSTP or IKEv2 — no VPN device needed
Site-to-Site (S2S) | On-premises network to Azure | IPsec (IKEv1 or IKEv2)
VNet-to-VNet | Encrypt connectivity between two VNets | IPsec (IKEv1 or IKEv2)
Multi-Site | Multiple on-prem sites into one VNet | Extension of Site-to-Site
You can create multiple connections off the same gateway — the one-per-VNet limit is on the gateway itself.
AZ-500 Skill 2.1 — Virtual Network Security
12

## Slide 14
VPN GATEWAY & AUTHENTICATION
Pre-Shared Keys and Point-to-Site Auth Options
Pre-shared key (PSK)
Auto-generated at tunnel creation — ASCII, up to 128 characters
Applies to both policy-based and route-based VPNs
Get-AzVirtualNetworkGatewayConnectionSharedKey — view
Set-AzVirtualNetworkGatewayConnectionSharedKey — change
P2S authentication options
Azure certificate — enterprise CA or self-signed root cert
RADIUS — also supports IKEv2/SSTP; only on VpnGw1/2/3 SKUs
Azure AD (Entra ID) — OpenVPN protocol only; Windows 10 requires the Azure VPN Client
MFA can be scoped to just VPN users via Conditional Access, without requiring it org-wide
Scenario cue: needs existing RADIUS/cert infrastructure → RADIUS. Gateway itself must validate the cert → native Azure certificate auth.
AZ-500 Skill 2.1 — Virtual Network Security
13

## Slide 15
POINT-TO-SITE / SITE-TO-SITE
P2S Protocol Comparison and S2S Prerequisites
Protocol | Advantages | Limitations
OpenVPN | TLS-based, traverses most firewalls; broad OS support (Android, iOS 11+, Windows, Linux, macOS 10.13+) | No Basic SKU; not on the classic deployment model
SSTP | Traverses most firewalls (TCP 443) | Windows only; capped at 128 concurrent connections regardless of SKU
IKEv2 | Standards-based IPsec; supports macOS 10.11+ | No Basic SKU; nonstandard UDP 500/4500 — must not be blocked client-side
Site-to-Site prerequisites
Compatible on-prem VPN device (policy-based or route-based) • Externally-facing public IPv4 address • On-prem address range Azure can route to
S2S and VNet-to-VNet both run over IPsec/IKE — the real difference is only what's sitting on the other end of the tunnel.
AZ-500 Skill 2.1 — Virtual Network Security
14

## Slide 16
VIRTUAL WAN
Hub-and-Spoke Connectivity at Global Scale
Virtual WAN's hubs connect in a full mesh over the Microsoft backbone — any-to-any connectivity without you wiring up every path yourself.
What plugs into a hub
Branch offices — via VPN / SD-WAN devices
End users — via Azure VPN client, OpenVPN, or IKEv2 (Point-to-Site)
Headquarters — via ExpressRoute circuits
Virtual networks — as spokes
Azure regions act as the hubs, and a standard Virtual WAN connects them in full mesh
A secured virtual hub adds Azure Firewall directly in the hub — inspection without routing traffic back out to a spoke first.
AZ-500 Skill 2.1 — Virtual Network Security
15

## Slide 17
VIRTUAL WAN
Planning Considerations
Partner NVAs (Barracuda, Cisco, VMware, Versa, Aruba) can deploy into a hub — but aren't required; any IKEv1/IKEv2-IPsec-compliant device works
1,000 connections per virtual hub
One on-prem device can connect to multiple hubs, via the closest Microsoft network edge
An NVA can be deployed inside a virtual hub
A spoke VNet connected to a hub cannot also have its own VNet gateway, and cannot have a route server
BGP is supported for VPN connectivity
ExpressRoute per-site is not required; multiple hubs are allowed in the same region
Default egress preference favors ExpressRoute over VPN (customizable)
Portal-created hubs must share the Virtual WAN's resource group — cross-RG hubs require PowerShell
These are the details that separate "knows Virtual WAN exists" from "can design with it" — treat them as first-class facts, not footnotes.
AZ-500 Skill 2.1 — Virtual Network Security
16

## Slide 18
ENCRYPTION OVER EXPRESSROUTE
MACsec vs. IPsec — Two Independent Layers
 | MACsec | IPsec
Layer | 2 — MAC-level | 3 — IP-level
Scope | Encrypts everything on the circuit, including BGP control traffic — all-or-nothing | End-to-end, e.g. on-prem to VNet
Requires | ExpressRoute Direct only; disabled by default | No ExpressRoute Direct requirement
Key management | Bring your own key, stored in Azure Key Vault — you own rotation | N/A
MACsec is pre-shared-key only — updating the key means updating both sides. A mismatch breaks traffic; plan a maintenance window.
AZ-500 Skill 2.1 — Virtual Network Security
17

## Slide 19
PAAS FIREWALLS
Firewall Settings on PaaS Resources (Azure Storage Example)
Storage firewall rules are enforced across every protocol that can reach the account, including REST and SMB — but the default allows all networks.
Portal: Networking blade
Public Network Access — All networks (default), Selected networks + IPs, or Disabled
Network Routing — Microsoft Network Routing (enter near the client) vs. Internet Routing (enter near the storage endpoint)
PowerShell — quick lockdown
Update-AzStorageAccountNetworkRuleSet \
-ResourceGroupName "MyRG" -Name "mystorage" \
-DefaultAction Deny
Public Network Access starts wide open — locking it to Selected networks or Disabled is something you do, not something you inherit.
AZ-500 Skill 2.1 — Virtual Network Security
18

## Slide 20
NETWORK WATCHER
Diagnostic Tools
Built for IaaS — VMs, VNets, App Gateways, load balancers. Not for PaaS resources or web analytics.
Tool | What it does
IP Flow Verify | Simulates a packet; returns allow/deny against NSG + Azure Virtual Network Manager admin rules
Next Hop | Shows next hop type, IP, and route table ID for a destination — confirms whether routing is actually as intended
Effective Security Rules | The combined inbound/outbound rules actually enforced on a NIC (security + admin rules together)
Connection Troubleshoot | Root-causes connectivity issues, distinguishing platform problems from user misconfiguration
NSG Diagnostics | Debug traffic permission logic; verify NSG rule configuration is correct
VPN Troubleshoot | Diagnose gateway/connection issues — via Portal, PowerShell, CLI, or REST
Packet Capture | Captures traffic to/from a VM or scale set for deep, proactive or reactive analysis
AZ-500 Skill 2.1 — Virtual Network Security
19

## Slide 21
NETWORK WATCHER
Monitoring & Traffic Tools
Tool | What it does
Connection Monitor | End-to-end connection monitoring across hybrid and Azure-native deployments
Topology | Visual map of network infrastructure, spanning subscriptions, resource groups, and regions
Flow Logs | The definitive record of all network activity — throughput, compliance, intrusion detection
Traffic Analytics | Analyzes flow log data for traffic pattern and dynamics insight
The question to ask yourself for each exam scenario: which of these eleven tools actually answers what's being asked?
AZ-500 Skill 2.1 — Virtual Network Security
20

## Slide 22
EXAM TIPS
Five Callouts Worth Remembering
IP addressing — pay close attention to subnet IP scenarios and potential connectivity issues from misconfiguration
Routing scenarios — the exam usually hinges on a route that's missing or misconfigured, not one that's wrong
VPN protocol scenarios — read for which protocol is ruled out by client OS, gateway SKU, or firewall constraints
Virtual WAN — review the official migration/use-case scenarios, not just the feature list
Network Watcher — the test is usually about picking the right diagnostic tool for the scenario, not just knowing they all exist
AZ-500 Skill 2.1 — Virtual Network Security
21

## Slide 23
KEY TAKEAWAYS
Six Ideas to Carry Into the Exam
Peering ≠ segmentation — AllowVNetInBound is open by default and has to be deliberately overridden
ASGs reference a role, not an IP — but only one ASG per source and one per destination, per rule
User-defined routes beat default system routes — only when the more specific route actually exists
P2S auth method is constrained by protocol, gateway SKU, and client OS — not just preference
Virtual WAN has its own rules — a spoke on a hub can't also carry its own gateway or route server
Network Watcher is eleven distinct tools — matching the right one to the scenario is the actual skill
AZ-500 Skill 2.1 — Virtual Network Security
22

## Slide 24
Questions?
AZ-500 Skill 2.1 — Virtual Network Security
Joe Poyzer